## Slide 1
U
U
U
Test A
Test C
Test B
Drag Force and Pump Selection
You work at Diamler…
You are tasked by your project manager to get a comparison on some new
designs for Diamler trucks that have arrived from R&D. Then determine the best pump combination to achieve this fuel delivery.
Part 1 (Drag and Power)
You are given experimental data on the drag coefficients of each design. Your job is to get the drag coefficients and calculate power values, savings, and metrics of comparisons. More is described in the emails sent by the project manager.
Part 2 (Pump Selection)
With the givens power requirement now move into sizing an optimum fuel pump. You are given pump performance data, efficiency data, combustion data and more. Remember you want to get the operating point as close as you can to the BEP of the pump. Use your imagination as to how to do this.

## Slide 2: Power Train Team, They don't report performance in terms of a head. You can get the density from Combustion or estimate it. Let's just go [SI] for the analysis. We can switch to barlycorn units at the end when we go to pitch. You'll probably have to combine two of these pumps. Just add the performance curves. For the efficiency curves combine them using a geometric mean. Project Manager, Sam Shaw Mohler
Team Emails
For this project the requirements will have to understood from
a series of internal emails at Daimler. An example of these emails is given on the right. They are included in the spreadsheet for the project.
There are 3 characters in this game.
Project Manager (Me..?)
Caleb Turner (Team Lead for Engine Systems)
A former marine and a hell of an engineer. He cut his teeth in the air-force as a flight mechanic for apache helicopters before college and then work. He thinks out of the box and has come up with a series of notes describing a new method of pump selection given combustion data.
Karl Cardin (Team Lead for Combustion)
Swedish by descent and learned chem eng. at Stanford, not the most vocal engineer. He has developed fuel additives that have increased yields twice in his career. He is a great resource for properties of the fuel and measurement methods.
NOTE: I was going to make fake emails so these characters could act like NPCs in video games or D&D campaigns….but I decided to drop that idea and just get it done. I also didn’t know if it was worth it to go through all that that cause some may not want to treat this like a video game. There is even a “cheat-code” I worked into this game. I realized part way through all this maybe is not fair cause some people don’t like video games so what’s left is just the story.

## Slide 3
What To Turn In
I want the documents asked for in the emails. All conclusions can be shown using plots. Defend your reasoning using math, scaling, etc.
Single Submission: Recorded PowerPoint w/Slides OR Written Report Paper.
Group Submission: Recorded Power Point AND Paper.
Your scribes have an extra role as well! They have to document the project and turn in the project diary at the end.
2) Your excel sheet any analysis was done on. Include charts/graphs/curves that prove your conclusions. You are provided a 4 page excel sheet but just submit a single sheet combining all your analysis. I also want all your slides.
Grading
Grading will basically be the exact same as project one. You will be graded on the clarity of your results. In an applied setting you have to prove to me beyond a reasonable doubt you’re analysis is correct. We are essentially lawyers of physics…
Due Date
June 8th
2 Points Extra Credit Every Day Early
2 Points Docked Everyday Late.

## Slide 4
A Grade Student Does…
  You deliver all the information asked for in the vague emails. This demonstrates you have the ability to not be a useless engineer if a problem isn’t stated in perfectly defined textbook academic fantasy land terms.
  Your plots are easy to understand and clear conclusions can be drawn from them.
  Your presentation/written report gives sound reasons for the design choice you recommend.
  You’ve found a way to tie every metric back to a cost savings. Money is all anyone cares about.
  You found the best operating point that considers combustion efficiency AND pump efficiency.
  You include some statistics in your analysis since everything is coming from raw data for this project. Nothing super fancy, just basic stuff.
  You mathematically optimize instead of heuristically optimize (A+) this means I’m okay if you just guess and check but that above and beyond gets the gold.
  You answer the secret question hidden within the emails (A+) I really took a lot of inspiration from video games…for this one.

## Slide 5: Group Submissions
You can keep the same group but you have to change roles. Basically same roles but I’ll lay it out again.
Team Lead (1)
  Presents Power Point, keeps team on track, edits/proof reads any docs, thinks big picture doesn’t waste time with detailed calculations, lowest grade of team of poor performance.
Technical Analysts (1-3)
  The detailed calculators, create plots for scribes, presents technical concerns to the team lead about data,
Scribes(1-3)
  Writes and compiles actual written documents to be turned in, thinks about crafting the story and not the technical details (understands them roughly from speaking and listening in meetings though), takes notes during any meetings to compile a project journal to be turned in at the end (this is new!)