## Slide 1
Pump
OHSU
q ~ 1.2o
h = 450 ft
Part 1: Water Delivery (Difficulty Level = Medium)
Pipe has 12 different diameters {Dk}, 4 Non-Circular Sections,
16 components {Ki}, (valves, readers, elbows, etc.),
and it made of two different pipe materials {e1, e2}
(75% of the pipe was restored from the original
1950 materials).
Refer to Excel data for these values.
What is the Power Requirement of the Pump?
Ref. Example 8.9 Munson to get Power…

## Slide 2: Quantities I Want.
Cost to run the pump per day.
Cost Increase Per Hospital Bed.
Cost if I made all the diameters the same value D. This could increase or decrease flow rate but the hospital is willing to make operational changes if its worth it.
  D = Geometric Mean: Are these cost savings worth it?
  D = Arithmetic mean: Are these cost savings worth it?
  Find the proper D to maintain the original required flowrate (Pipe Sizing Problem Iteration will be required, yuck).
Cost to run if I replaced all the Pipes with Commercial Steel
  Are these cost savings worth it?

## Slide 3
Part 2: Water Distribution. (Difficulty Level = Legendary)
Pump
Level 2, H = 15 ft, Q = 1.5-4.5 gal/min
Level 1, H = 0, Q = 2.5-6.5 gal/min
Level 3, H = 30 ft, Q = 1.5-3.6 gal/min
Ball Valve, Open, D = 8 in
Ball Valve, Open, D = 8 in
The first part was to pump water into a local hospital tank. This tank is always considerably full the new problem is
To distribute the water to the hospital levels. Design for maximum and minimum flow rate requirements per level.
Refer to the excel data sheet for the data on the piping system dimensions and components.
7 pipe dimensions and components
7 pipe dimensions and components
7 pipe dimensions and components

## Slide 4: Quantities I Want.
Cost to run the pump at all floors maximum flowrate
Cost to run the pump at all floors minimum flowrate
Savings if I remodeled all the piping to Commercial Steel
(Extra Credit) Should I just have a water pump per floor? Some googling on pump sizes may answer this given a power requirement per floor vs power requirement for the building.

## Slide 5: Grade Rubric: This is real/applied life like you all wanted so no right answers just your boss’s opinion on how well you did, how clearly you presented results, and how detailed you decided to get. How well you do effects your job. My response to your project is expressed in [text].
D-F Project: Student did not include minor losses, presents results in graphs and charts with no labels or axes, inputs random numbers in their excel chart (if I click on your Reynolds or friction factor cell it better be a formula!) Only completes part of Part 1, gives up on Part 2, Only delivers the cost of the pump no comparison questions. Delivers just an excel sheet with numbers with no text to guide me. Some numbers aren’t even labeled so I’ll have to rework what they are from formulas. Tons of unit errors.
[You’re fired, I don’t know why we hired you]

## Slide 6: Grade Rubric
C: Completes some Part 1 questions: Results are given in plots and charts but no explanation of how I should interpret the results. There is a chart floating in an excel chart with an axes but no clear labeling of what it means. Major mistakes in some formulas as well. You have a couple unit errors. You also give no reasoning for the methods you took to get your numbers. This is when I will have to go thru and check your formulas manually to verify mistakes I find. So you will be making my life a living hell. [You’re not getting that promotion]

## Slide 7: Grade Rubric
B: Completes all of Part 1 and some Part 2 questions: Submits a written document or power point slides that are well written but still take time for me to digest how to use your graphs and excel sheet. Luckily the document helps me along and it doesn’t take me too much time. I also find small minor errors in your assumptions (i.e. you forgot contraction losses between different diameters, wrong friction factor formula, forgot hydraulic diameter.). Maybe found one unit error. You give a good analysis though and I can give a confident answer. [You stay at current position with a nice Christmas bonus]

## Slide 8: Grade Rubric
A: Completes all questions of Part 1 and Part 2. Graphs are clear for interpretation and idiot proof. You make assumptions, but defend them on a quantitative basis, (i.e. I didn’t consider the angled pipe because it only add x% compared to ignoring it). Submits a recorded Power Point presenting of their results to me your boss and my bosses as well (The board is coming down on my ass about this pump budget so don’t mess this up for me.) No more than 10 minutes. Brief and clear preferred. [Lets talk in my office later about that promotion!]
A+: All of A requirements and also adds another design insight I for how/we could save money. [I’m retiring soon and I think you should have my job]

## Slide 9: Group Submission (Optional)
If you want to divide and conquer this will be difficult, but I’m so into it. (I don’t even know if this is okay to do for PSU grades wise…)
Some things will change for grading teams though. You are required to record a Power-Point and write a 5-10 page document if you want to do teams. Division of labor should make you more productive so I’d expect all group submission to be at least a B. You can’t skip Part 2.
If you submit as a group notice you are required to submit a report, excel sheet, and presentation. If you are doing an individual submission you have the option of power point slide OR written document.
  You need to submit to me a team member list but April 5th. With required roles.

## Slide 10: Team Lead Role
Team Lead: You have to give the presentation. The quality of the project no matter who touches it falls on you. Team leads sometimes have to redo their employees work late at night.
Pros: You’re not on the line for calculations, but you do have to direct your team and make sure no errors are occurring, if you’re not checking in and making sure you’re getting right answers then you’re in trouble. Bug them, make them work.
Cons: You’re team grade is on the line if I can’t understand your presentation and its not clear or definitely wrong. I will give you a lower grade than your team if your team did poorly. That’s the gamble you take by accepting this role, you can’t let anyone slack cause you’re on the hook. Maximum Allowed: 1 & Minimum: 1

## Slide 11: Analyst Role
Technical Analyst(s): You will have to do the calculations and listen to whatever it is your team lead tells you to do. You’re making the excel sheet on this one. The quality of the excel sheet regardless of who touches it falls on you.
Pros: You get to be a number monkey and that’s it (better be right though).
Cons: You better be right, all of you if all you have to do is calculate then I better not find calculation errors. Lowest grade in analysis is shared amongst all analysts…correct each other. Maximum Allowed: 3 & Minimum: 1

## Slide 12: Scribe Role
Scribe(s): You will actually prepare the submission and be a conduit between the analyst and the team lead. If you need a graph or number ask your analyst don’t make it that’s their job. The quality of the report regardless of who edits it falls on you.
Pros: You’re good at writing and can help the analysts get their point across without doing the grunt work.
Cons: You’re writing will be graded and picked apart, you have to understand these calculations to write about them. Lowest grade in writing is shared amongst scribes…share and review. Maximum Allowed: 2 & Minimum: 1

## Slide 13: Summary
Grade | F-D | C | B | A
Part One | Some quantities | Everything besides pipe sizing problem | All | All
Part Two | None | None | Some | All
Unit Errors | Lots | Some | Some | Few
Plots | Poorly Labeled | Labeled | Labeled + Correct Margins | Labeled+ Correct Margins
Conclusions | Mostly false | This costs more | This costs more because… | This costs more because…
Excel Sheet | I can’t use it | Works, hard to figure out what cells is linked to what. | Works, medium to figure out. I can re-engineer it. | Works, super simple to use. Beautiful formatting nice on the eyes.
Writing | Typos everywhere, I don’t even understand what you’re talking about | Some typos, clear message though. Took me two reads. | I understand because I’m teaching the class | Very simple and clear. Not wordy. No jargon. Yet short? (the paradox of writing…..)