## Slide 1
U
U
U
Test A
Test C
Test B
Drag Force and Pump Selection
You work at Diamler…
You are tasked by your project manager to get a comparison on some new
designs for Diamler trucks that have arrived from R&D. Then determine the best pump combination to achieve this fuel delivery.
Part 1 (Drag and Power)
You are given experimental data on the drag coefficients of each design. Your job is to get the drag coefficient and calculate power values, savings, and metrics of comparison. More is described in the emails sent by the project manager.
Part 2 (Pump Selection)
With the givens power requirement now move into sizing an optimum fuel pump. You are given pump performance data, efficiency data, combustion data and more. Remember you want to get the operating point as close as you can to the BEP of the pump.

## Slide 2: Power Train Team, They don't report performance in terms of a head. You can get the density from Combustion or estimate it. Let's just go [SI] for the analysis. We can switch to barlycorn units at the end when we go to pitch. You'll probably have to combine two of these pumps. Just add the performance curves. For the efficiency curves combine them using a geometric mean. Project Manager, Sam Shaw Mohler
Team Emails
For this project the requirements will have to understood from
a series of internal emails at Daimler. An example of these emails is given on the right. They are included in the spreadsheet for the project.
There are 3 characters in this game.
Project Manager (Me..?)
Caleb Turner (Team Lead for Engine Systems)
A former marine and a hell of an engineer. He cut his teeth in the air-force as a flight mechanic for apache helicopters before college and then work. He thinks out of the box and has come up with a series of notes describing a new method of pump selection given combustion data.
Karl Cardin (Team Lead for Combustion)
Swedish by descent and learned chemistry at not the most verbal engineer.
He has developed fuel additives that have increased yields twice in his career. He is a great resource for properties of the fuel and measurements
NOTE: I was going to make fake emails so these characters could act like NPCs in video games or D&D campaigns….but I decided to drop that idea and just get it done. I also didn’t know if it was worth it to go through that cause some may not want to treat this like a video game. There is even a “cheat-code” I worked into this game. I realized part way through all this maybe its not fair cause some people don’t like video games so what’s left is just the story.

## Slide 3
What To Turn In
1)
Single Submission: Recorded PowerPoint + Slides or Written Report Paper. Explaining your analysis.
Group Submission: Recorded Power Point AND Paper.
2) Your excel sheet any analysis was done on. Include charts/graphs/curves that prove your conclusions. You are provided a 4 page excel sheet but just submit a single sheet combining all your analysis.
Grading
Grading will basically be the exact same as project one. You will be graded on the clarity of your results. In an applied setting you have to prove to me beyond a reasonable doubt you’re analysis is correct.

## Slide 4
A Student Does…
  You deliver all the information asked for in the vague emails. This demonstrates you have the ability to not be useless if a problem isn’t stated in perfectly defined textbook academic fantasy land terms.
  You plots are easy to understand and clear conclusions can be drawn from them.
  Your presentation/written report gives sound reasons for the design choice you recommend.
  You’ve found a way to tie every metric back to a cost savings. Money is all anyone cares about.
  You found the best operating point that considers combustion efficiency AND pump efficiency.
  You include some statistics in your analysis since everything is coming from raw data for this project.
  You mathematically optimize instead of heuristically optimize (A+)
  You answer the secret question hidden within the emails (A+) I really took a lot of inspiration from video games…for this one.